## Slide 1: Water Supply, Sanitation and Hygiene Promotion (WASH)
Lutheran World Information image

## Slide 2: By the end of this session you will be able to:
Explain the primary objective and three essential concepts behind WASH programming
Identify the main transmission pathways of infectious pathogens and barriers to break the chains of transmission
Use some of the technical numerical indicators with enhanced confidence and understanding
Relate the quantitative technical aspects of Sphere to its foundational rights-based aspects
Notes: Present the session objectives, informing the participants that this presentation will be a survey of the WASH chapter in the Sphere Handbook, but it will not cover every Indicator, key action, and guidance note. It will highlight some of the indicators that are easiest to visualise and grasp through experiential learning, so that otherwise obscure numbers can be comprehended “in human terms.” This will also empower non-technicians to better work in multi-functional teams, better understand WASH sectoral reporting, and to contribute to inter-sectoral coordination discussions in an informed way. The session is also designed to highlight the links between the foundational chapters of Sphere and the technical chapters.
The session also highlights the evaluation phase of the programme cycle, although the guidance in this chapter equally applies to all phases of the cycle.
Ask if there are any WASH specialists or experts in the group. If so ask them to briefly explain their experience and work, and ask if they would be comfortable to serve as “expert resources” for the session.

## Slide 3: Objective of WASH programmes
The main objective of WASH programmes in humanitarian response is to reduce public health risks by creating barriers along transmission pathways.
The main pathways for pathogens to infect humans are faeces, fluids, fingers, flies and food (also known as the five Fs)
Notes: Before using the animation on this slide, ask participants if they can name the five main pathways through which pathogens infect the human body.

## Slide 4: The F diagram
Barriers can stop the transmission of disease; these can be:
        primary (preventing the initial contact with the faeces); or
  secondary (preventing it being ingested by another person).
They can be controlled by WASH interventions.
Source: Water, Engineering and Development Centre (WEDC)
See page 144
Notes: Refer participants to this diagram in the Sphere Handbook. Ask them to give examples of some of the barriers, e.g. “how can we separate faeces from the environment so that flies cannot access it?” or “does anyone have an example of a fly control programme activity?”
Take a minute to point out that there are three additional “Fs” in the diagram: floods, fields, and faeces.

## Slide 5: There are six categories of WASH standards
Water supply
Hygiene promotion
WASH in disease outbreaks and healthcare settings
Solid waste management
Excreta management
Vector control
Each category has its own standard(s)
Standard 1.1
Hygiene promotion
Standard 1.2
Identification, access, and use of hygiene items
Standard 1.3
Menstrual hygiene management and incontinence
Standard 2.1
Access and water quantity
Standard 2.2 Water quality
Standard 3.1
Environment free from human excreta
Standard 3.2
Access to and use of toilets
Standard 3.3
Management and maintenance of excreta collection, transport, disposal, and treatment
Standard 5.1
Environment free from solid waste
Standard 5.2
Household and personal actions to control vectors
Standard 5.3
Solid waste management systems at community level
Standard 6
WASH in healthcare settings
Standard 4.1
Vector control at settlement level
Standard 4.2
Household and personal actions to control vectors
See page 90
5
Notes: Explain that this presentation is not intended to explore each individual standard in depth, but rather to provide a broad understanding of the standards and their application. The presentation will highlight one to two of the standards within each of the six categories of standards. This slide simply explains the structure and general content of the chapter – it is not intended as an in-depth discussion of each standard.

## Slide 6: The six categories of standards can be linked to establishing barriers along the five pathways
Water supply
Hygiene promotion
WASH in disease outbreaks and healthcare settings
Solid waste management
Excreta management
Vector control
6
Notes: Small-group activity:
When this slide appears, DO NOT CLICK FORWARD UNTIL IT IS TIME TO DEBRIEF THE ACTIVITY. Distribute envelopes to each table containing the 12 pre-cut “F markers”. These are made using the file STP 7 WASH F markers.docx. Ensure each table has a flip chart and a marker. Also distribute the exercise instructions (1 per group) in the file STP 7 WASH Activity.docx.
Participants will need small bits of tape handy to fix the markers to their flipcharts.
Allow about 5 minutes for this quick activity. The debrief will be a simple comparison of the different flipcharts prepared by the groups, followed by the reveal of the “textbook answer” using the slide animation.
Debrief: Emphasise that these are all connected, and this is a simplified representation to illustrate the six categories of standards as a whole. It also explains the logic of the content of the six Sphere WASH themes.

## Slide 7: Three essential WASH concepts
People affected by crises are more susceptible to illness and death from disease, particularly diarrhoeal and infectious diseases.
Such diseases are strongly related to inadequate sanitation and water supplies, and poor hygiene.
WASH programmes aim to reduce public health risks.
IFRC/Sajid Hasan
Notes: Review these concepts (from page 92), and underscore that these ideas form the basis of all WASH programming.

## Slide 8: Based on this aim, the key WASH activities are:
promoting good hygiene practices;
providing safe drinking water;
providing appropriate sanitation facilities;
reducing environmental health risks; and
ensuring conditions that allow people to live with good health, dignity, comfort, and safety.
Australian Red Cross/Antony Balmain
Notes: Ask participants to provide an example of a programme that is designed around each activity, such as a handwashing programme at schools for good hygiene practices or a well ring construction cash-for-work programme for providing safe drinking water.
NOTE: “Environmental health” is not defined in the Sphere Handbook. For our purposes, any risk factor that constitutes a public health risk in the environment near or surrounding a population is to be considered an environmental health risk. For clarity, you can use examples such as stagnant water as it can be a breeding ground for vectors such as malaria-transporting mosquitoes, or snails and flat worms which would increase the risk of schistosomiasis. Programmes designed to provide better drainage can be used as examples that address these risks. Shallow graves, or graves or latrines in close proximity to wells, are also good examples of environmental health risks.

## Slide 9: In WASH programmes
It is important to manage the entire water chain:
water sourcing;
treatment;
distribution;
collection;
household storage; and
consumption.
IFRC/Corrie Butler
Notes: The importance of managing the water chain is highlighted since contamination of water can happen at any point between sourcing and consumption. Failure to plan and monitor activities at each link may result in failure of the entire system.

## Slide 10: In WASH programmes
It is important to:
manage the entire sanitation chain in an integrated manner;
enable positive healthy behaviours; and
ensure access to hygiene items.
Australian Red Cross
Notes: This notes the importance of hygiene promotion and the need for soap as a distribution (or otherwise made available) item.
NOTE: The sanitation chain is the process through which waste water, excreta and greywater moves from contamination to its end points of reuse or disposal. Managing the chain will protect people from exposure to disease-causing excreta and other such risks. The chain moves from containment through emptying, transport, and treatment, ending in reuse or disposal. Some entities will refer to the elements of waste water and excreta separately using the excreta flow diagram with reference to the latter. For more information, refer participants to the WHO Sanitation Safety Planning (SSP) manual.

## Slide 11: Community engagement is at the centre of all WASH Activities
Context
Advocacy
Coordination and collaboration
Monitoring, evaluation, accountability and learning
Participation
Accountability
Capacity building
People
Behaviour and practice
Information and communication
See page 93
Notes: Ask participants to open their Sphere Handbook to page 93. Ask for a volunteer to read the first full paragraph on the page aloud:
“Engaging with the community creates an essential understanding of perceptions, needs, coping mechanisms, capacities, existing norms, leadership structures and priorities, as well as the appropriate actions to take. Monitoring and evaluation, including feedback mechanisms, demonstrate whether WASH responses are appropriate or need to be adjusted. ⊕ see Core Humanitarian Standard commitments 4 and 5.”

## Slide 12: WASH in the broader context?
See page 50
Notes: Remind the participants of the nine commitments of the Core Humanitarian Standard. Note in particular commitments 4 and 5:
Commitment 4 – Communities and people affected by the crisis know their rights and entitlements, have access to information and participate in decisions that affect them (page 63).
Commitment 5 – Communities and people affected by crisis have access to safe and responsive mechanisms to handle complaints (page 66).
Ask participants for examples of how these two commitments (related to a WASH programme) might be evaluated in an ongoing response.

## Slide 13: Section 1: Hygiene promotion
People are aware of key public health risks related to WASH, and can adopt individual, household and community measures to reduce them.
Hygiene promotion
Standard 1.1
Hygiene promotion
Standard 1.2
Identification, access, and use of hygiene items
Standard 1.3
Menstrual hygiene management and incontinence
IFRC/Sajid Hasan
Notes: This is a simple review of the standards in the hygiene promotion theme.
For standard 1.1, ask participants to quickly refer to the indicators on page 97. Ask what they notice about this list of indicators. (They are almost all progress indictors.) The meaning of this is that the benchmarks for these percentages are not known or globally agreed yet the need for monitoring this information is critical. It highlights the need to establish these baselines quickly and monitor progress over time.
For standards 1.2 and 1.3, ask what hygiene items, and how much/many are needed, in an emergency response (per person) where people are displaced and do not have ready access to these items. Refer participants to pages 100 and 102.
Tactile/visualisation exercise – bring along 250 grams of soap to illustrate how much this is. Pass the bar around and ask if this seems like enough for 1 person for 1 month.

## Slide 14: Standard 2.1: Access and water quantity
People have equitable and affordable access to a sufficient quantity of safe water to meet their drinking and domestic needs.
Water supply
Standard 2.1
Access and water quantity
Standard 2.2 Water quality
Lutheran World Federation/C Kästner
Notes: Before proceeding to the next slide, ask how many litres per day participants think they consume. Ask how many litres would be the minimum for a life with dignity. Explain that Sphere provides guidance for this and proceed to the next slides.

## Slide 15: Key indicators of standard 2.1
Average volume of water used for drinking and domestic hygiene per household
Minimum of 15 litres per person per day
Determine quantity based on context and phase of response
See page 107
Notes: Be clear that the number of 15 litres per person per day is only an indicator, but a very useful one.
As per the table shown (from page 107), 7.5–15 litres is based on drinking and domestic hygiene only. Depending on the context, this may be insufficient for life with dignity.
For example, a Muslim population may require more water than a non-Muslim population due to religious practices such as prayer preparation.
The table on page 145 expands on this one, and may be used to answer questions about water quantities needed for diverse uses.

## Slide 16: Water math
Visualising water quantities
1 metre
1 metre
1 metre
1 litre
10 cm
10 cm
1 litre of water = 1 kg
1 m3 of water = 1,000 litres
1 m3 of water = 1,000 kg
1 m3 of water = 1 metric ton
1 cubic meter = 1 metric ton
Notes: This slide illustrates the way water is represented in assessments, reports and evaluations. Understanding this basic definitional and mathematical foundation will make it possible for users to properly apply the Sphere indicators and better understand discussions of various water programming issues.
Tactile/visualisation exercise: As a physical demonstration, provide a 1 litre bottle, and 10, 15 and 20 litre jerry cans filled with water. These will help participants visualise the volumes and feel the weight of water. Ask them to identify the volumes in each and pass them around.

## Slide 17: Key indicators of standard 2.1 (continued)
Distance from any household to the nearest waterpoint: 500 metres
Queuing time at water sources: <30 minutes
Maximum of 250 people per tap (based on a flow rate of 7.5 litres/minute)
Photo: LWF/ C. Kästner
Lutheran World Federation/C Kästner
Notes: Review the key figures on the slide.
Tactile/visualisation exercise continued: This is a great opportunity to get your participants moving, and energised, while allowing them the opportunity to gain a tactile understanding of some of the Sphere WASH indicators.
Pre-fill at least one jerry can that holds 15 litres of water and pre-measure a distance of 25 metres in any nearby location (in the training room, corridor, or nearby outdoor area). Ask for volunteers (at least one man and one woman) to carry the jerry can(s) 25 metres, turn around and come back (i.e. 50 metres in total).
Ask volunteers if that was easy. Then, ask if they could easily do it another nine times? Explain that after walking that distance 10 times, they will still only have enough water for one family member for the day. Ask participants to raise their hands if any of them are from a family of one. Then ask who typically carries water in a refugee camp or other such setting (women and children). Have a couple more volunteers repeat the exercise. Resume the presentation within 10 minutes.
NOTE: A more advanced form of this exercise also incorporates flow rates and queueing. If a tap is available, create a course in which participants carry empty jerry cans 50 metres, fill them from the tap, then return with them filled. Start several participants at the same time, or in reasonably quick succession. Other participants could measure the flow rate and assess queuing times.

## Slide 18: Key indicators of standard 2.2: water quality
Percentage of water quality tests meeting minimum water quality standards
<10 colony forming units (CFUs)/100ml at point of delivery (unchlorinated water)
≥0.2-0.5mg/l free residual chlorine (FRC) at point of delivery of delivery (chlorinated water)
Turbidity of less than 5 nephelometric turbidity units (NTU)
See page 110
Notes: If you have water testing tools, here is a great opportunity to show participants what they are and how they can be used. Two very simple ways to illustrate turbidity are:
Fill a large barrel, bucket, or basin with murky water. If you have a turbidity stick (a 90 cm long stick with a black and white patterned disk on one end), lower it into the water and show the participants how the visibility of the stick differs with depth. NTU of 5 will be when the disk can no longer be seen through about 85cm of water (roughly the length from shoulder to fingertips).
Alternatively, fill three clear plastic water bottles (with the labels removed) with equal amounts of water and a small amount of soil the night before the presentation. Shake them up for the same amount of time and place them in the training room. Before the session, shake two of the bottles. When you are done reading the content of this slide shake one of the two bottles. This should allow for a clear distinction in the turbidity of all three bottles. Explain that water storage can be a contributing factor in the water purification process as allowing water to settle can decrease its turbidity (allowing it to be separated from the sediment within the container before the purification process). Water clarity does not indicate safety (or vice versa as coffee is safe to drink), but it does indicate if the water is clear enough to further treat with chlorine.

## Slide 19: What does <5 NTU mean?
<5 NTU
>5 NTU
>100 NTU
This is a measure of water clarity, to determine if water is clear enough to chlorinate efficiently.
InterWorks photo
19
Notes: If you do not have access to materials described in the previous slide, use this image to explain what turbidity means, and to show a rough idea of how clear the water needs to be to allow effective chlorination. Note that in the middle bottle, the text can still be made out through the cloudy water. In simplest terms, 5 NTU means that the water is pretty clear.

## Slide 20: Key indicators of standard 3.2: Access to and use of toilets
Ratio of shared toilets
Minimum 1 per 20 people
Distance between dwelling and shared toilet
Maximum 50 metres
% of toilets that have internal locks and adequate lighting
% of toilets reported as safe by women and girls
% of women and girls satisfied with the menstrual hygiene management options at toilets they regularly use
Notes: Explain these indicators and ask participants to consider how each of these affect protection and dignity concerns. (Reference Protection Principle 1 – Enhance people’s safety, dignity and rights and avoid exposing them to further harm.)
Take a few moments here as a follow-on discussion to highlight links between this technical chapter and the foundation chapters. Ask participants, for example:
How does Protection Principle 2 relate to this chapter? (Ensure people’s access to impartial assistance, according to need and without discrimination.)
Which of the nine commitments of the CHS are closely interlinked with the WASH sector? Answer: All of them! Refer participants to the diagram on page 50 for a quick review.

## Slide 21: Let’s do a quick evaluation mission
We’ll travel to Uganda to evaluate a WASH programme being run by Oxfam. Watch the video that follows and answer these evaluation questions.
From the information provided by the engineer:
Is water quantity sufficient?
Is water quality sufficient?
Who else would you like to talk to, and what would you ask?
Notes: Explain that the group will do a quick evaluation mission to Uganda, using some of the information just covered in this session, as well as other standards, actions, indicators, and guidance not explicitly presented. Ask participants to make a quick note of the three questions before going on the mission (viewing the video that follows on the next slide).

## Slide 22: Let’s design an evaluation
Notes: Show the video, which includes a lot of positivity about the WASH programme being implemented.
Ask participants – working individually – to watch it with a critical eye, and to note any specific information provided.
On YouTube: https://www.youtube.com/watch?v=61R2CuPr3t8
Click “cc” in the video to view subtitles.

## Slide 23: Evaluation mission
From the information provided by the engineer:
Is water quantity sufficient?
Is water quality sufficient?
Who else would you like to talk to, and what would you ask?
Figures stated
98,000 refugees
105 storage tanks at 10m3 each
Water tankers provide 584,000 litres/day of treated water
Notes: Ask participants (working together at their tables or in groups of five or six people) to answer the three questions using whatever parts of Sphere are useful.
As a tip, use the animation on this slide to reveal the numbers that were provided by the engineer.
If they are unclear about how to proceed, ask participants to review the indicators for quality and quantity, as well as to think about the potential challenges not mentioned in the video, but identifiable from what is shown (jerry cans, water pumps, length of lines at water points, general attitude of people using the facilities, etc.).
Allow about 15 minutes for the group work.
Once the time has passed, call for contributions, asking each group in turn to provide just one answer or key point. Continue until all groups have provided at least one answer. Some of the maths work and textbook answers are provided in the notes view on the next slide.

## Slide 24: Evaluation mission
From the information provided by the engineer:
Is water quantity sufficient?
Is water quality sufficient?
Who else would you like to talk to, and what would you ask?
Notes: Textbook answers:
The water quantity is too low based only on the information given. 98,000 refugees x 15 l/p/day = 1,470,000 litres required daily. The mount provided by the Oxfam trucks was reported to be 584,000 l/day. While this is a red flag, note that there may be other programmes also contributing water beyond Oxfam’s fleet, and refugees may have access to other water sources. Also, remind everyone that if people are satisfied and healthy, the standard is being met – even if this indicator is not. Failure to meet an indicator means we must look farther and at other aspects to determine if the standard it supports is being met or not. People who are washing clothes and looking happy are not thirsty. However, this may indicate that water is not being distributed fairly, rather than there being an excess. Unfair distribution and wastage challenge the otherwise “simple” maths formula of 15 x number of people: those that get to the tap first may use and take more than their fair share.
Water quality is addressed in principle, but not proven. The engineer refers to turbidity, bacteriological contamination (e-coli), and residual chlorine. These are all in line with the Sphere water quality indicators, but test results are not made clear. Note that if people are satisfied and healthy, this is another indicator that water quality is probably acceptable.
Who else to talk to: It would be a mistake in an evaluation of a WASH programme to only talk to the WASH programme engineer. Evaluators should talk to community leaders, facility users (women and children), as well as technicians. Evaluation should also include questions to other responders to understand the totality of the response, and how the Oxfam programme integrates with them. Other questions to ask include forward-planning questions on coming rainy seasons, the quality of roads in all seasons, sustainability of the water tinkering (purification) system, etc.
Review the CHS. All of the nine commitments should also be evaluated as they relate to the WASH response.
Note that evaluations in this sector must also investigate community involvement, feedback mechanisms, and other community participation-related aspects – not just quality and quantity.

## Slide 25: Key messages
The main objective of WASH programmes in humanitarian response is to reduce public health risks by creating barriers along transmission pathways.
Community engagement is at the centre of all WASH programming.
WASH programming does not only concern hand washing, water quantity and quality.
Monitoring and evaluation are essential components of any WASH programme.